# Ttalk

by Bud Krueger

How's your ZDDP?

A serious oil issue for our cars

The following material was recently posted on The MG Enthusiasts' BB and is MUST READING for all of us who are working at keeping our cars on the road. It looks as if our trusty old Castrol GTX 20W50 has changed.

OIL IS KILLING OUR CARS!!!!!

By: Keith Ansell, Foreign Parts Positively, Inc.

About a year ago I read about the reduction of zinc dithiophosphate (ZDDP) in the oils supplied with API approval that could affect sliding and high pressure (EP) friction in our cars. The reduction of these chemicals in supplied oil was based on the fact that zinc, manganese and/or phosphates reduce the effectiveness and eventually damage catalytic converters and introduce minute amounts of pollutants into our atmosphere.

A month or so ago I had a member of the Columbia Gorge MG Club bring a totally failed camshaft and lifters back to me that had only 900 miles on them!! I immediately contacted the camshaft re-grinder and asked how this could happen. They were well aware of this problem as they were starting to have many failures of this type. In the past, the lack of a molybdenum disulfide camshaft assembly lubricant, at assembly, was about the only thing that could create this type of problem. My customer has assembled many engines and had lubricated the camshaft properly and followed correct break in procedures.

This got me on the phone to Delta Camshaft, one of our major suppliers. Then the bad news came out: It’s today’s “modern” API (American Petroleum Industry) approved oils that are killing our engines.

Next call: To another major camshaft supplier, both stock and performance (Crane). They now have an additive for whatever oil you are using during break-in so that the camshaft and lifters won’t fail in an unreasonably short period of time. They also suggest using a diesel rated oil on flat tappet engines.

Next call: To a racing oil manufacturer that we use for the race cars (Redline). Their response: “We are well aware of the problem and we still use the correct amounts of those additives in our products”. They continued to tell me they are not producing API approved oils so they don’t have to test and comply. Their oils were NOT the “new, improved and approved” ones that destroy flat tappet engines! “We just build the best lubricants possible”. Sounds stupid, doesn’t it, New-Approved but inferior products, but it seems to be true for our cars.

To top this off: Our representative from a major supplier of performance and street engine parts (EPWI) stopped by to “warn us” of the problem of the NEW oils on flat tappet engines. This was a call that the representative was making only because of this problem to warn their engine builders! “The reduction of the zinc, manganese and phosphates are causing very early destruction of cams and followers”. They are recommending that, for now at least, there must be a proper oil additive put in the first oil used on new engines, beyond the liberal use of molydisulfide assembly lube. They have been told that the first oil is the time the additives are needed but remain skeptical that the first change is all that is necessary. Their statement: Use diesel rated oils such as Delo or Rotella that are usually available at auto stores and gas stations.

This problem is BIG! American Engine Rebuilder's Association (AERA) Bulletin #TB2333 directly addresses this problem. I had a short discussion with their engineer and he agreed with all that I had been finding.

Next phone call was to a retired engineer from Clevite, a major bearing and component manufacturer. First surprise was that he restored older British Motor bikes. The second surprise was that he was “VERY” aware of this problem because many of the old bikes had rectangular tappets that couldn’t rotate and are having a very large problem with the new oils. He has written an article for the British Bike community that verify all the “bad news” we have been finding.

Comp Cams put out “#225 Tech Bulletin: Flat Tappet Camshafts”. They have both an assembly lube and an oil additive. The telling sentence in the bulletin was “While this additive was originally developed specifically for break-in protection, subsequent testing has proven the durability benefits of its long term use. This special blend of additives promotes proper break-in and protects against premature cam and lifter failure by replacing some of the beneficial ingredients that the oil companies have been required to remove from the off the–shelf oil”.

Next question: Now what do we do?

From the camshaft re-grinders (DeltaCam) “Use oils rated for diesel use”, Delo (Standard Oil product) was named. About the same price as other quality petroleum based oils. They are not API formulated and have the zinc dithiophosphate we need in weights we are familiar with.

From the camshaft manufacturer (Crane): “use our additive” for at least the first 500 miles.

From General Motors (Chevrolet): add EOS, their oil fortifier, to your oil, it’s only about $12.00 for each oil change for an 8 ounce can (This problem seems to be something GM has known about for some time!).

From Redline Oil: Use our street formulated synthetics. They have what we need!

From our major oil distributor: Distributing Castro, Redline, Valvoline and Industrial oils: “After over a week of contacts we have verified that the major oil companies are aware of the problem”. “The representatives of the oil companies today are only aware of marketing programs and have no knowledge of formulation”. The only major oil companies they were aware of for doing anything to address this are Valvoline that is offering an “Off Road 20W-50” and Redline.

From Castrol: We are beginning to see a pattern emerging on older cars. It may be advantageous to use a non-approved lubricant, such as oils that are Diesel rated, 4 Cycle Motorcycle oils and other specified diesel oils.

Last question: So what are we at Foreign Parts Positively going to do? After much research we are switching to Redline Street rated oils and stocking the Castrol products that are diesel rated. Castrol, owned by British Petroleum, is now just a brand name. This is a difficult decision as we have been a dealer and great believer in all Castrol Products for over 40 years. We have been using Castrol Syntech oil in new engines for about 3 years so the cost difference in changing to Redline is minimal. The actual cost in operation is also less as the additive package in Redline makes a 1-year or up to 18,000 mile change recommended! Yes, it is a long change interval but with lowered sulfur levels and the elimination of lead and many other chemicals in the fuels there are less contaminants in our oil from the fuel, which is the major contributor to oil degradation. We will continue to offer the Castrol products but will now only stock the suggested diesel oils that they produce.

Too many things are starting to show up on this subject and it has cost us money and time. Be aware that “New and Improved”, or even products we have been using for many years, are destroying our cars as it isn’t the same stuff we were getting even a year ago.

For the cars that use “engine oil” in their gearboxes this may even pose a problem as these additives that have been removed could be very critical in gear wear. We will be using oil specifically formulated for Manual Gearboxes with Brass Synchronizers. The only oils we are aware of that fit the criteria are from General Motors and Redline.

If you have any additional input let us know. We need to let every flat tappet engine owner, i.e.: every British Car owner know that things are changing and we MUST meet the challenge.

Keith Ansell, President

Foreign Parts Positively, Inc.

www.ForeignPartsPositively.com

360-882-3596

* * * * *

About Keith:

Keith Ansell, Owner, started his career in 1962 as an apprentice mechanic in a nationally known shop. After completing his apprenticeship he worked for British Motor Car Distributors as a line mechanic. Foreign Parts Positively (also known as FPP) was started in the fall of 1969 in Aloha, Oregon. FPP has been in existence since that time, building the present facility in 2001. Keith has trained and is experienced on most British cars from 1936 to 1980. Raced MGA twin-cam and MGA MKII Deluxe, A.H. Sprite, Lotus 18 and built many successful SCCA race cars, H Production 948 AH Sprites to MGBs. Member British Motor Trade Association, NAMGAR, NAMGBR, Columbia Gorge MGA Club & Willamette MG Club..

* * * * *

This thread on the UKMGBBS has lead to an indication that there may only be a few oils worth using, e.g., Redline 10W40 or Valvoline VR1 Racing Oil, 20W50.  This is being written in mid-October to meet the publication deadline and, by the time you read it, there may well be others that will be found to meet our needs. More recent information will be available on my website at http://www.ttalk.info/ZDDP.htm.

Bud Krueger

admin@ttalk.info